PC to the device*3

| Command (1 byte) | Picture Number (1 byte) | Rolling Code (2 byte) | Data Byte (192 byte)*1 | Check Sum (1 byte)(Count by PC) | Note |
| --- | --- | --- | --- | --- | --- |
| 01H | 01H( OLED1) | From (00H 00H), (00H C0H), to the last | To show each pixel of RGB in PC | Command + Picture Number + Rolling Code + Data byte | To download OLED1 data |
| 01H | 02H( OLED2) | From (00H 00H), (00H C0H), to the last | To show each pixel of RGB in PC | Command + Picture Number + Rolling Code + Data byte | To download OLED2 data |
| 01H | 03H( OLED3) | From (00H 00H), (00H C0H), to the last | To show each pixel of RGB in PC | Command + Picture Number + Rolling Code + Data byte | To download OLED3 data |
| 02H | 00H | 00H 00H | 00H(192 byte) | 02H | Power ON*4 |
| 03H | 00H | 00H 00H | 00H(192 byte) | 03H | Power OFF*5 |
| 04H | 01H | 00H 00H | 00H(192 byte) | 05H | To show OLED1 |
| 04H | 02H | 00H 00H | 00H(192 byte) | 06H | To show OLED2 |
| 04H | 03H | 00H 00H | 00H(192 byte) | 07H | To show OLED3 |
| 07H | 00H | Two bytes of ID code | 00H(192 byte) | 07H + Two bytes of ID code | Write ID code to the device |
| 08H | 00H | 00H 00H | 00H(192 byte) | 08H | To ask ID code of the device |
| 09H | 20D | 00H 00H | 00H(192 byte) | 09H+20D | Brightness 20% |
| 09H | 40D | 00H 00H | 00H(192 byte) | 09H+40D | Brightness 40% |
| 09H | 60D | 00H 00H | 00H(192 byte) | 09H+60D | Brightness 60% |

The device to PC*2

| Command Type | Data | Note |
| --- | --- | --- |
| 00H | Check Sum (Command + Picture Number + Rolling Code + Data byte) (1 byte)(Count by the device) | To let PC check the data is correct or not, so all of the protocol will follow this, expect the button data from the device to PC |
| 01H | 01H(button 1) | To let PC know the button is pushed |
| 01H | 02H(button 2) | To let PC know the button is pushed |
| 01H | 03H(button 3) | To let PC know the button is pushed |
| 02H | Two bytes of ID code | To let PC know the ID of the device*6 |

*1 The total data of the picture is 96*96*2(16 bits interface of OLED) bytes, and we send the data from PC to the device, each time will be 192 bytes, so we can send just 96 times.

*2 The data from the device to PC is 2 bytes, so PC can be easy to check.

*3 If the device has some problems, it can’t receive the correct data and make the correct response. PC needs to send 00H, until the device also sends 00H to PC, then sends the data from the beginning again.

*4 When the device is plugged into PC, PC can send the data to the external ram, then show the OLED, after these two parts, then power on the OLED. Because we power on first, the user will see the random picture in the OLED.

*5 For the working life consideration of the OLED, we need to send power off before the device is unplugged from PC.

*6 When PC sends the protocol to ask the ID of the device, we will send three bytes to PC. This is the only one protocol form the device to PC that will send three bytes. Others are two bytes.