The communication method between Host and the Optimus keyboard

Ver. 0.7

- Basic concept

  - The Host could be PC or MAC.

  - Transmitting information by MSD between host computer t and keyboard.

  - It is necessary for Keyboard to have one SD card as MSD.

  - The OLED picture of user’s application program should be stored in SD card.

  - The OLED dynamic picture and commands should transfer to a virtual file which located in keyboard too.

  - The virtual files are located in the next disk order of SD card, i.e. SD card is E: thus the virtual disk’s direction will be F: .

- The procedure

  - The default format contends some folders and files, please refer to table 1.

  - The keyboard firmware will read the default picture of OLED from SD and display it

Commands

- Table 1:

| File name | Description | Location | Format |
| --- | --- | --- | --- |
| /vOptimus/upgrade.bin | It’s a write-only file, to upgrade firmware | virtual disk | “_upgrade” + firmware data + checksum (two bytes) |
| /vOptimus/order.sys | To adjust the brightness of OLED | virtual disk | “b”+xxx + (“A”) xxx if the base of OLED brightness, from 001 to 100. Enable the environmental luminance automatic adjustment function if “A” is added at the end of the command. |
| /vOptimus/version.sys | It’s a read-only file, to store the firmware version information | virtual disk | “OptimusVxx.xx” , xx.xx is firmware version number, Ex. “OptimusV01.00”. |
| /vOptimus/present.sys | It’s a read-only file, to illustrate the OLED present information | virtual disk | The format is 114-bytes data, each byte represents a certain OLED exists or not, “1” means OLED exit, and “0” means OLED has not installed, begin from the first OLED (#001) to the last one (#114). ( The OLED map please refer to appendix A.) |
| /vOptimus/layout.sys | It’s a write-only file, to switch OLED layout. | virtual disk | The format is 114-bytes data, each byte represents which layout will be displayed on the OLED, 0x00 : To display default layout. 0x01 : To display dynamic picture. |
| /vOptimus/normal/xxx.sys | To real-time update default OLED picture of normal operation, xxx is OLED number: 001 to 114. | virtual disk | Two bytes for one pixel, from OLED’s upper left corner to lower right corner, 4608 bytes total. * |
| /vOptimus/shift/xxx.sys | To real-time update default OLED picture while “shift-key pressing” or “Num-Luck” or “Caps Lock”, xxx is OLED number: 001 to 114. | virtual disk | Two bytes for one pixel, from OLED’s upper left corner to lower right corner, 4608 bytes total. * |
| /vOptimus/dynamic/xxx.sys | To display dynamic OLED picture of normal operation, xxx is OLED number: 001 to 114. | virtual disk | Two bytes for one pixel, from OLED’s upper left corner to lower right corner, 4608 bytes total. * |
| /Optimus/normal/xxx.sys | The default OLED picture of normal operation, xxx is OLED number: 001 to 114. | SD card | Two bytes for one pixel, from OLED’s upper left corner to lower right corner, 4608 bytes total. * |
| /Optimus/shift/xxx.sys | The default OLED picture while “shift-key pressing” or “Num-Luck” or “Caps Lock”, xxx is OLED number: 001 to 114. | SD card | Two bytes for one pixel, from OLED’s upper left corner to lower right corner, 4608 bytes total. * |
| /Optimus/scancode.sys | To store the default keypad scan-code. | SD card | Each Key has 64 Bytes scan-code, total 9216 Bytes. ( The key map please refer to appendix B.) Every two bytes represent a movement. The byte 1 represent : 0xFF : ending code Bit0 : standard key function if this bit set to 1 Bit1 : key make (press key) if this bit set to 1 Bit2 : key break (release key) if this bit set to 1 The byte 2 represent scan-code, please refer to table 2 Ex. Let keyboard send " B " " B " " B " three in succession " B" Check table 2, “B”=0x05 To press key is 02H ,and to release key is 0x04 Thus the code-code will be : 0x02,0x05,0x04,0x05,0x02,0x05,0x04,0x05,0x02,0x05, 0x04,0x05,0xFF,0xFF,0xFF,0xFF |
| / vOptimus/ scancode.sys | It’s a write-only file, To real-time update scancode. | virtual disk | Ditto |

* - The bitmap of OLED 003 and 014 should rotate 90 degrees clockwise first.

Table 2:

| Key Define | Key code (HEX) | Key Define | Key code(HEX) | Key Define | Key code(HEX) | Key Define | Key code(HEX) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 00H | 0 | key_p | 13 | key_9 | 26 | key_cap | 39 |
| 00H | 1 | key_q | 14 | key_0 | 27 | key_f1 | 3A |
| 01h | 2 | key_r | 15 | key_enter | 28 | key_f2 | 3B |
| key_undefine | 3 | key_s | 16 | key_esc | 29 | key_f3 | 3C |
| key_a | 4 | key_t | 17 | key_bs | 2A | key_F4 | 3D |
| key_b | 5 | key_u | 18 | key_tab | 2B | key_f5 | 3E |
| key_c | 6 | key_v | 19 | key_space | 2C | key_F6 | 3F |
| key_d | 7 | key_w | 1A | key_neg | 2D | key_f7 | 40 |
| key_e | 8 | key_x | 1B | key_equation | 2E | key_f8 | 41 |
| key_f | 9 | key_y | 1C | key_L_brackets | 2F | key_f9 | 42 |
| key_g | A | key_z | 1D | key_R_brackets | 30 | key_f10 | 43 |
| key_h | B | key_1 | 1E | key_code29 (/) | 31 | key_f11 | 44 |
| key_i | C | key_2 | 1F | key_code42 | 32 | key_f12 | 45 |
| key_j | D | key_3 | 20 | key_semicolon | 33 | key_print | 46 |
| key_k | E | key_4 | 21 | key_apostrophe | 34 | key_scroll | 47 |
| key_l | F | key_5 | 22 | key_tilde (~) | 35 | key_pause | 48 |
| key_m | 10 | key_6 | 23 | key_comma | 36 | key_insert | 49 |
| key_n | 11 | key_7 | 24 | key_dot | 37 | key_home | 4A |
| key_o | 12 | key_8 | 25 | key_interrogation | 38 | key_pgup | 4B |
| key_del | 4C | key_num_0 | 62 | key_r_alt | 78 | key_undo | 8E |
| key_end | 4D | key_num_dot | 63 | key_r_win | 79 | key_copy | 8F |
| key_pgdn | 4E | key_code45 | 64 | key_help | 7A | key_cut | 90 |
| key_R_arrow | 4F | key_app | 65 | key_mute | 7B | key_paste | 91 |
| key_L_arrow | 50 | key_padequ | 66 | key_vol_down | 7C | key_office_home | 92 |
| key_dn_arrow | 51 | key_f13 | 67 | key_vol_up | 7D | key_www_home | 93 |
| key_Up_arrow | 52 | key_f14 | 68 | key_word | 7E | key_www_back | 94 |
| key_num_lock | 53 | key_f15 | 69 | key_excel | 7F | key_www_forward | 95 |
| key_num_div | 54 | key_code107 | 6A | key_mail | 80 | key_redo | 96 |
| key_num_star | 55 | key_code56 | 6B | key_calender | 81 | key_reply | 97 |
| key_num_neg | 56 | key_code133 | 6C | key_calculator | 82 | key_forward | 98 |
| key_num_plus | 57 | key_code14 | 6D | key_log_off | 83 | key_send | 99 |
| key_num_enter | 58 | key_code132 | 6E | key_app_l | 84 | key_next_track | 9A |
| key_num_1 | 59 | key_code131 | 6F | key_app_r | 85 | key_pre_track | 9B |
| key_num_2 | 5A | key_151_Hangul | 70 | key_task_pane | 86 | key_stop | 9C |
| key_num_3 | 5B | Key_150_Hanja | 71 | key_spell | 87 | key_play | 9D |
| key_num_4 | 5C | key_L_ctrl | 72 | key_files | 88 | key_media_sel | 9E |
| key_num_5 | 5D | key_l_shift | 73 | key_new | 89 | key_my_computer | 9F |
| key_num_6 | 5E | key_l_alt | 74 | key_open | 8A | key_www_search | A0 |
| key_num_7 | 5F | key_L_win | 75 | key_close | 8B | key_www_stop | A1 |
| key_num_8 | 60 | key_r_ctrl | 76 | key_save | 8C | key_www_refresh | A2 |
| key_num_9 | 61 | key_r_shift | 77 | key_f12_print | 8D | key_www_favorites | A3 |
| key_power | A4 |  |  |  |  |  |  |
| key_sleep | A5 |  |  |  |  |  |  |
| key_wake_up | A6 |  |  |  |  |  |  |
| key_fn | A7 |  |  |  |  |  |  |

Appendix A : OLED number Map

* Dummy OLED number: 007

Appendix B : Key number Map

*Dummy Key number: 89,94,106,107,108,112,114~118,120,122~126,128,130~134,136,138~144